|  | Inc. | MEMORANDUM Bothell Crossroads Project |
| --- | --- | --- |

Date:		April 23, 2009

To:		Michael Booth, Perteet, Environmental Project Manager

Steve Morikawa, City of Bothell, Capital Projects Manager

From: 		Jim Rothwell, Ecologist

Re:		Summary of Wetland Delineation Results

Background

Perteet, Inc. has performed a wetland delineation and field investigation at the Bothell Crossroads/SR 522 project site.  The wetland, referred to as Wetland A (Map-Page 10) for the purposes of this memorandum, is located between State Route (SR) 522 and the Sammamish River and south of NE 180th Street.  The delineation took place in May 2008, with subsequent visits performed in January and April 2009 to obtain additional information.

Technical Guidance and Determinations

Based on the U.S. Fish and Wildlife Service (USFWS) classification system (Cowardin et al. 1979), Wetland A is primarily a palustrine emergent and palustrine forested system.  Based on the hydrogeomorphic (HGM) classification system (Brinson 1993), Wetland A is a depressional outflow system, although sloped areas are present as well.  Wetland A received a Category III rating under the Washington State Department of Ecology Wetland Rating System for Western Washington (Hruby 2004).  According to the Bothell Municipal Code, section 14.04.530(F), Category III wetlands require a 75-foot buffer and 15-foot building setback.

Dominant vegetation in Wetland A includes reed canarygrass (Phalaris arundinacea), red alder (Alnus rubra), black cottonwood (Populus balsamifera), and willow species (Salix sp.).  A representative soil profile exhibited matrix colors of black (2.5Y 2.5/1) to a depth of 4 inches, dark gray (10YR 4/1) between 4 and 8 inches, and black (10YR 2/1) below 8 inches.  The soil texture was silty clay to a depth of 20 inches.  In addition, oxidized rhizospheres (root channels) were present within the upper 12 inches of the soil profile.  Other soil profiles contained redoximorphic features (i.e. mottles) with varying colors, including dark yellowish brown (10YR 4/6), gray (10YR 5/1), and dark brown (7.5YR 3/4).  The soils were saturated to the surface during the field investigation.  A small stream enters the wetland along its western boundary, flows into a ponded area, and then exits the wetland before connecting to the Sammamish River.  Wetland A extends off-site to the south of the project area.

Based on the results of the delineation, Wetland A meets the specific criteria for a wetland determination as outlined in the Washington State Wetlands Identification and Delineation Manual (WDOE 1997).  The dominant vegetation in the wetland has an indicator status of facultative (FAC) or wetter; soils exhibited low-chroma colors below 10 inches (the depth at which indicators must appear for a soil to meet hydric criteria) and contained redoximorphic features; and wetland hydrology was present in the form of soil saturation to the surface.

Upland areas adjacent to Wetland A are dominated by red alder, black cottonwood, Himalayan blackberry (Rubus armeniacus), and reed canarygrass.  Soils are very dark grayish brown (10YR 3/2) loam to depth of 12 inches, dark brown (10YR 3/3) sandy loam between 12 and 16 inches, and dark grayish brown (10YR 4/2) sand below 16 inches.  Redoximorphic features are present below 12 inches and are dark yellowish brown (10YR 4/4, 4/6), gray (10YR 5/1), and light brownish gray (10YR 6/2) in color.  Saturated soil, free water, and other wetland hydrology indicators were not observed in the upland areas.

The forested area that is located immediately north of Wetland A and south of NE 180th Street was mapped as wetland during two previous delineations in 1992.  However, based on the data collected by Perteet biologists, this area does not currently meet wetland criteria.  Approximately 17 years have passed since the earlier delineations were performed, and it is very likely that conditions throughout the forested area have changed significantly.  While hydrophytic vegetation and/or hydric soils were present at some of the test plots, wetland hydrology was not observed at any of the locations.  Regardless of wetland status, this forested area is significant as it has a direct connection to Wetland A and provides some wildlife habitat.

All of the vegetation, soil, and hydrology data from the delineation is included in the wetland data forms (attached).   Should you have any questions or comments, please do not hesitate to contact Jim Rothwell, Ecologist or Michael Booth for further clarification.

Enc: Wetland data forms

References

Brinson, M.M. 1993.  A Hydrogeomorphic Classification for Wetlands.  Technical Report WRP-DE-4.  U.S. Army Engineer Waterways Experiment Station, Vicksburg, Mississippi. August 1993.

Cowardin, L.M., V. Carter, F.C. Golet, and E.T. LaRoe.  1979.  Classification of Wetlands and Deepwater Habitats of the United States.  Publication FWS/OBS-79/31.  U.S. Department of the Interior, Fish and Wildlife Service, Office of Biological Services.

Ecology.  1997.  Washington State Wetlands Identification and Delineation Manual.  Ecology Publication 96-94.  Washington State Department of Ecology, Olympia, Washington.

Hruby, T.  2004.  Washington State Wetland Rating System for Western Washington—Revised.  Ecology Publication 04-06-025.  Washington State Department of Ecology, Olympia, Washington.  August 2004.